## Slide 1
LUNA-SITE
Lunar South Pole Ice & Terrain Evaluation
Bharatiya Antariksh Hackathon 2026 · Challenge 8 · Chandrayaan-4 Mission Support
21-Layer AI Pipeline
Physics-Regularized CNN
NSGA-II Optimiser
RRT* Rover Planner
ISRO DFSAR Data
TEAM LUNA-SITE | Delhi Technological University

## Slide 2
THE PROBLEM
Why finding lunar ice is harder than it sounds
👁
The Optical Paradox
Permanently Shadowed Regions (PSRs) are the most likely places to find water ice — but no camera can see into them. They exist at –248 °C with zero photon flux. Every team that deploys YOLO inside a PSR has already lost.
🧠
The Black Box AI Trap
Sending a CNN result to ISRO without physics justification will be rejected. Decisions about landing sites must be explainable to scientists. CPR, DOP, and Grad-CAM heatmaps are not optional extras — they are the product.
⏱
The 30-Hour Compute Trap
Full-mission NSGA-II + RRT* over a 512×512 DEM takes 48+ hours on CPU. Teams that leave global optimisation to the finale will fail. All heavy computation must be pre-computed.
LUNA-SITE was designed to solve all three of these traps.

## Slide 3
21-LAYER ARCHITECTURE
Five phases, one unified pipeline
L0–L2
Phase 1
Data Ingestion
DFSAR Stokes
LOLA DEM
SPICE illum
L3–L9
Phase 2
Ice Detection
CPR/DOP gate
Physics-reg. CNN
MC Dropout + XAI
L10–L13
Phase 3
Hazard Mapping
Dual-zone YOLO/DEM
Traversability
Earth visibility
L14–L16
Phase 4
Site Selection
ISRU potential
NSGA-II Pareto
Multi-rover assign
L17–L20
Phase 5
Rover Plan
Energy RRT*
DWA local
Gazebo twin
KEY INNOVATIONS
✓ Dual-zone YOLO/radar switch
✓ Physics-regularized CNN (not a black box)
✓ Hungarian tracker (not DeepSORT)
✓ 75th-percentile depth bounds (not point estimates)

## Slide 4
LAYERS 3–8 | ICE DETECTION
From radar backscatter to confidence-bounded ice maps
Physics Gate — Layer 3
CPR = (S₁ – S₄) / (S₁ + S₄)
Circular Polarisation Ratio → ice >1.0
DOP = √(S₂²+S₃²+S₄²) / S₁
Degree of Polarisation → ice <0.13
Ice gate: CPR > 1.0 AND DOP < 0.13
Both criteria must be met simultaneously
L = λ / (4π √ε′ · tan δ)
Depth penetration equation (Layer 8 bounds)
Physics-Regularized CNN
4-channel Stokes → 3 classes (Ice/Rock/Regolith). Loss = CrossEntropy + λ·Physics_Penalty. NOT called a PINN — a PINN requires PDE embedding via autodiff. This is accurately described as physics-regularized.
MC Dropout (50 passes)
Dropout ON during inference. 50 stochastic forward passes → mean probability, epistemic variance, predictive entropy. Uncertainty maps shown alongside every prediction.
Grad-CAM Explainability
Heatmaps prove the CNN attends to CPR/DOP patterns, not crater geometry. ISRO-required XAI: every prediction has a spatial attribution map viewable in the dashboard.
75th-percentile depth bounds: L-band gives 1.30m–5.36m. P(ice within 2m drill limit) = 47% (L-band), 63% combined.

## Slide 5
LAYER 10 | DUAL-ZONE HAZARD MAPPING
The Optical Paradox — solved with a hardware-aware switch
☀️
Zone A — Sunlit Approach
OHRC optical + LOLA DEM slope
YOLOv8 detects boulders ≥ 0.32m (Chandrayaan-4 wheel clearance)
Slope map flags terrain > 10° (stability limit)
Boulder density × slope = combined hazard score
~73% safe pixels
🌑
Zone B — PSR Interior
LOLA DEM roughness + DFSAR texture ONLY
YOLOv8 is PHYSICALLY DISABLED
Temperature: 25 K. Photon flux: zero.
LOLA DEM RMS roughness proxies boulder hazard
DFSAR surface texture replaces optical detection
~61% safe pixels
Chandrayaan-4 hardware constraints enforced throughout: Max slope 10° · Boulder clearance 0.32m · Battery 100 Wh · Solar recharge 20W (sunlit only)

## Slide 6
LAYERS 14–16 | SITE SELECTION
NSGA-II multi-objective optimisation — 3 competing objectives
f₁ Maximise ice volume
(min –Ice/500)
f₂ Minimise terrain hazard
(min Hazard)
f₃ Maximise solar hours
(min –Solar/6)
PARETO FRONT — TOP 5 MISSION SITES (NSGA-II Rank 1)
Rank
Site ID
Ice Volume
Hazard
Solar h/day
P(drill)
CRM Score
Status
#1 ★
#31
159 m³
0.00
1.3
39%
0.426
SELECTED
#2
#36
83 m³
0.03
2.4
29%
0.458
Backup A
#3
#125
121 m³
0.03
1.8
54%
0.458
Backup B
#4
#66
47 m³
0.02
2.8
—
0.477
Contingency
#5
#12
52 m³
0.09
3.3
—
0.479
Contingency
CRM = 0.40 × Ice + 0.35 × Hazard + 0.15 × Solar + 0.10 × Earth-link | 200 candidates → 170 feasible → 16 Pareto-optimal

## Slide 7
LAYERS 17–18 | ROVER PLANNING
Energy-aware RRT* global path + DWA real-time obstacle avoidance
Energy-Aware RRT* (Global)
Traversal cost = Euclidean × (1 + slope_factor + shadow_penalty)
Slope factor: exponential near 10° limit
Shadow penalty: 1.5× in PSR (battery drain, no solar)
Asymptotically optimal — pre-computed before finale
DWA Local Obstacle Avoidance (Gazebo live)
Dynamic Window Approach runs at rover tick rate in Gazebo Digital Twin
Velocity sampling in [v_min,v_max] × [ω_min,ω_max] window
Scoring: 50% heading + 30% goal distance + 20% velocity
Handles new obstacles discovered during live traverse
Ported from MATLAB Combat Simulator
Kalman filter + Hungarian + RRT* + DWA stack originally built for drone swarm collision avoidance. Adapted for low-gravity, slow-speed lunar terrain. Python port validated on identical synthetic scenarios.
MISSION TRAVERSE STATS
Algorithm
RRT* + DWA
Waypoints
27 global
Path cost
435.6 (energy)
Max speed
1 cm/s (lunar)
Slope gate
< 10°
Obstacle radius
0.32m clearance
PSR cost mult.
1.5×
Pre-compute time
1.35s (CPU)
Finale strategy: RRT* pre-computed ✓ | DWA runs live in Gazebo Digital Twin | No 30-hour compute trap ✓

## Slide 8
LAYER 19 | MISSION DASHBOARD
Interactive mission control — 6 live modules
🌍
Lunar Maps
DEM · illumination · slope · Earth-vis
🧊
Ice Probability
CPR/DOP · CNN · uncertainty heatmaps
⚠️
Hazard Maps
Dual-zone · boulder density · traversability
🎯
Landing Sites
NSGA-II Pareto · site comparison · select
🤖
Rover Simulation
RRT* path · DWA avoidance · live telemetry
⚡
Battery & Power
14-day profile · solar harvest · PSR penalty
Built with Streamlit · Plotly · Physics-rendered terrain textures · All 21 pipeline layers exposed in real-time

## Slide 9
ARCHITECTURAL INTEGRITY
Flaws identified — and precisely fixed
✗ DeepSORT used for orbital cross-pass tracking
→
✓ Replaced with Hungarian Assignment — correct for sparse orbital passes (days/weeks apart, no appearance embeddings)
✗ CNN called 'PINN' without PDE embedding
→
✓ Renamed to Physics-Regularized CNN. True PINN embeds PDEs via autodiff. Ours adds physics penalty to CE loss — accurate terminology
✗ YOLO enabled inside PSR — the Optical Paradox
→
✓ Dual-zone switch: YOLO strictly disabled in PSR. Only LOLA DEM + DFSAR roughness used at 25K zero-light zones
✗ Depth given as a single point estimate
→
✓ 75th-percentile bounds via 10,000 tan-δ samples. Output is P(ice within drill limit) — honest to ISRO scientists
✗ MC Dropout disabled at inference (eval mode)
→
✓ enable_mc_dropout() explicitly re-enables Dropout layers after model.eval(). 50 stochastic passes with correct uncertainty

## Slide 10
ROADMAP TO FINALE
What's built · What's next · Why we win
✅ BUILT & TESTED
✓ CPR/DOP physics gate with roughness rejection
✓ Hungarian orbit tracker (3 passes validated)
✓ Physics-regularized CNN (Grad-CAM + MC Dropout)
✓ Depth probability bounds (L + S band)
✓ Dual-zone hazard mapper (YOLO off in PSR)
✓ NSGA-II Pareto front (16 rank-1 sites)
✓ Energy-aware RRT* (27 waypoints, 1.35s CPU)
✓ DWA local avoidance (Gazebo-ready)
✓ Streamlit Mission Control dashboard (6 modules)
✓ Synthetic DFSAR dataset (2000 samples)
🔧 BEFORE FINALE
⚠ Parse 1 real DFSAR .img from ISRO PRADAN
⚠ Train CNN on real patches (even 50 tiles)
⚠ Build minimal Gazebo world (flat + obstacles)
○ Export TorchScript model for real-time inference
○ Pin requirements.txt + Dockerfile
○ Faustini / Shackleton cross-validation
○ Science validation against Hayne et al. 2015
Architecture is finalist-ready. The bridge between design and deployment is 4 weeks of real-data work.

## Slide 11
LUNA-SITE
Lighting the path to lunar water — for Chandrayaan-4 and beyond
21
Pipeline layers
3
Objectives (NSGA-II)
16
Pareto-optimal sites
47%
P(ice ≤ 2m depth)
27
RRT* waypoints
5
Architectural flaws fixed
Bharatiya Antariksh Hackathon 2026 · Challenge 8 · Team LUNA-SITE · Delhi Technological University